Title
Logic Control Chart
Logic Control Chart: A Better Visual Language
Presented By: M.A.Sc Candidate FanFan Huang
[Speaker Notes: Good Afternoon everyone and thank you all for coming In this seminar we will look at Programmable Logic controllers. And a new visual metaphor for programming them. Programmable logic controllers predate micro-controllers and are widely used in heavy industrial sectors. Due to the short amount of time in this presentation I'll be focusing on the usage of the languages rather then the syntax of these languages.]

---
System Overview
Software and Graphical User Interface Layer
Hardware Abstraction Layer
Chip Tools Layer
Tools
Start Block
Store Block
Input Block
Output Block
Delay Block
Canvas
Zoom
Scroll
File Processor
(Save / Load)
Memory
Model
Trace
Engine
program.c
plcmcu.mcp
plcmcu.h
plcmcu.c
Chip Specific C Compiler
Simulator
Compiler
[Speaker Notes: So this is the system that was developed as a whole hardware and software. I tried to keep things simple where possible but the end result is still pretty massive. Arrows in this diagram represent data flow throughout the program. This isn't exact as there are some details I choose to omit to fit it on the slide.]

---
System Overview
Software and Graphical User Interface Layer
Tools
Start Block
Store Block
Input Block
Output Block
Delay Block
Canvas
Zoom
Scroll
File Processor
(Save / Load)
Memory
Model
Trace
Engine
Simulator
Compiler
[Speaker Notes: So this is the system that was developed as a whole hardware and software. I tried to keep things simple where possible but the end result is still pretty massive. Arrows in this diagram represent data flow throughout the program. This isn't exact as there are some details I choose to omit to fit it on the slide.]

---
Logic Control Chart
- A visual metaphor based on State Machines
- Goal: Easy!
- Reads like a flow chart
- Based on UML2 specification for State Machine Diagrams
- UI designed to mimic popular flow charting software like Microsoft Visio, and Open Office Draw.
[Speaker Notes: So we felt that it was important for PLC's to maintain their visual programming. But we also felt that Ladder Logic has been vastly outdated. For one we wanted to bring in the ability of sequencing things easily since most programmers trained these days are used to the concept of doing things sequentially. Human beings in general seem to also solve problems in a sequential manner. Logic control chart was designed to read much like a flow chart, as it was felt this universally understandable by all. Logic control chart was loosely based off the UML2 specification for State Machine Diagrams it was rigorous enough to form our foundation and contained all the concepts I would need to build my own language. Obviously I had to modify a few things to bring it to the level of concreteness that I can compile actual useful code but overall it's pretty close. Now I'll have a tool demo right after this slide but a main goal was to make things easier. This also goes for the actual IDE, there's no point of putting all this effort into creating a language that's super easy if the IDE is loaded with tools and foreign concepts. So for that I looked to Microsoft Visio for inspiration on existing chart drawing tools.]

---
Tool Overview
- Canvas
- Block Tools
- Compilation Tools
- Simulation Tools
[Speaker Notes: Open tool: Parts of the UI: Canvas, Tool pallet, Menu bar, Compile and simulation. Selection, Connectors. Usage of the drawing canvas: Draw a simple program, show how variable edits are made. (see blinky.xml) Hit compile show the compiled code Hit simulation show the simulated code]

---
Simulator View
- Simulator:
  - Trace the code
  - View memory

---
Logic Control Chart
- Language Components
- Start
- Delay
- Input
- Output
- Store
- Edges
[Speaker Notes: In logic control chart if you can understand flow charts you can pretty much read the program. We only have 5 blocks but are able to do any logic. Again the emphasis here is simple see are sticking to the fundamentals Start block is an anchoring tool it really does nothing else but tell our program to start in that state. Edges for us are branch statements it allows you to branch based on conditionals in the guard conditions. Input and Output allows you to interact with the outside world through your I/O pins. The store block is very flexible it's used to both store variables and also to perform calculations. It also supports multi-line allowing you to compute things in one block. Multi-line store blocks are done in sequence. The delay block allows you to wait for a short period of time useful for timing applications, you can do the same with a loop and a counter but it's less accurate.]

---
Logic Control Chart
- Language Components
- Start
- Delay
- Input
- Output
- Store
- Edges
[Speaker Notes: In logic control chart if you can understand flow charts you can pretty much read the program. We only have 5 blocks but are able to do any logic. Again the emphasis here is simple see are sticking to the fundamentals Start block is an anchoring tool it really does nothing else but tell our program to start in that state. Edges for us are branch statements it allows you to branch based on conditionals in the guard conditions. Input and Output allows you to interact with the outside world through your I/O pins. The store block is very flexible it's used to both store variables and also to perform calculations. It also supports multi-line allowing you to compute things in one block. Multi-line store blocks are done in sequence. The delay block allows you to wait for a short period of time useful for timing applications, you can do the same with a loop and a counter but it's less accurate.]

---
Logic Control Chart
- Language Components
- Start
- Delay
- Input
- Output
- Store
- Edges
[Speaker Notes: In logic control chart if you can understand flow charts you can pretty much read the program. We only have 5 blocks but are able to do any logic. Again the emphasis here is simple see are sticking to the fundamentals Start block is an anchoring tool it really does nothing else but tell our program to start in that state. Edges for us are branch statements it allows you to branch based on conditionals in the guard conditions. Input and Output allows you to interact with the outside world through your I/O pins. The store block is very flexible it's used to both store variables and also to perform calculations. It also supports multi-line allowing you to compute things in one block. Multi-line store blocks are done in sequence. The delay block allows you to wait for a short period of time useful for timing applications, you can do the same with a loop and a counter but it's less accurate.]

---
Logic Control Chart
- Language Components
- Start
- Delay
- Input
- Output
- Store
- Edges
[Speaker Notes: In logic control chart if you can understand flow charts you can pretty much read the program. We only have 5 blocks but are able to do any logic. Again the emphasis here is simple see are sticking to the fundamentals Start block is an anchoring tool it really does nothing else but tell our program to start in that state. Edges for us are branch statements it allows you to branch based on conditionals in the guard conditions. Input and Output allows you to interact with the outside world through your I/O pins. The store block is very flexible it's used to both store variables and also to perform calculations. It also supports multi-line allowing you to compute things in one block. Multi-line store blocks are done in sequence. The delay block allows you to wait for a short period of time useful for timing applications, you can do the same with a loop and a counter but it's less accurate.]

---
Logic Control Chart
- Language Components
- Start
- Delay
- Input
- Output
- Store
- Edges
[Speaker Notes: In logic control chart if you can understand flow charts you can pretty much read the program. We only have 5 blocks but are able to do any logic. Again the emphasis here is simple see are sticking to the fundamentals Start block is an anchoring tool it really does nothing else but tell our program to start in that state. Edges for us are branch statements it allows you to branch based on conditionals in the guard conditions. Input and Output allows you to interact with the outside world through your I/O pins. The store block is very flexible it's used to both store variables and also to perform calculations. It also supports multi-line allowing you to compute things in one block. Multi-line store blocks are done in sequence. The delay block allows you to wait for a short period of time useful for timing applications, you can do the same with a loop and a counter but it's less accurate.]

---
Logic Control Chart
- Language Components
- Start
- Delay
- Input
- Output
- Store
- Edges
[Speaker Notes: In logic control chart if you can understand flow charts you can pretty much read the program. We only have 5 blocks but are able to do any logic. Again the emphasis here is simple see are sticking to the fundamentals Start block is an anchoring tool it really does nothing else but tell our program to start in that state. Edges for us are branch statements it allows you to branch based on conditionals in the guard conditions. Input and Output allows you to interact with the outside world through your I/O pins. The store block is very flexible it's used to both store variables and also to perform calculations. It also supports multi-line allowing you to compute things in one block. Multi-line store blocks are done in sequence. The delay block allows you to wait for a short period of time useful for timing applications, you can do the same with a loop and a counter but it's less accurate.]

---
Logic Control Chart
- Language Components
- Start
- Delay
- Input
- Output
- Store
- Edges
[Speaker Notes: In logic control chart if you can understand flow charts you can pretty much read the program. We only have 5 blocks but are able to do any logic. Again the emphasis here is simple see are sticking to the fundamentals Start block is an anchoring tool it really does nothing else but tell our program to start in that state. Edges for us are branch statements it allows you to branch based on conditionals in the guard conditions. Input and Output allows you to interact with the outside world through your I/O pins. The store block is very flexible it's used to both store variables and also to perform calculations. It also supports multi-line allowing you to compute things in one block. Multi-line store blocks are done in sequence. The delay block allows you to wait for a short period of time useful for timing applications, you can do the same with a loop and a counter but it's less accurate.]

---
Logic Control Chart
- Language Components
- Start
- Delay
- Input
- Output
- Store
- Edges
[Speaker Notes: In logic control chart if you can understand flow charts you can pretty much read the program. We only have 5 blocks but are able to do any logic. Again the emphasis here is simple see are sticking to the fundamentals Start block is an anchoring tool it really does nothing else but tell our program to start in that state. Edges for us are branch statements it allows you to branch based on conditionals in the guard conditions. Input and Output allows you to interact with the outside world through your I/O pins. The store block is very flexible it's used to both store variables and also to perform calculations. It also supports multi-line allowing you to compute things in one block. Multi-line store blocks are done in sequence. The delay block allows you to wait for a short period of time useful for timing applications, you can do the same with a loop and a counter but it's less accurate.]

---
Example: Blinky Light
[Speaker Notes: Here we have an example of a light that simply blinks on and off. (more to add here! Will be added once demo run-throughs are practised)]

---
Old vs New

---
System Overview
Software and Graphical User Interface Layer
Hardware Abstraction Layer
Chip Tools Layer
Tools
Start Block
Store Block
Input Block
Output Block
Delay Block
Canvas
Zoom
Scroll
File Processor
(Save / Load)
Memory
Model
Trace
Engine
program.c
plcmcu.mcp
plcmcu.h
plcmcu.c
Chip Specific C Compiler
Simulator
Compiler
[Speaker Notes: So this is the system that was developed as a whole hardware and software. I tried to keep things simple where possible but the end result is still pretty massive. Arrows in this diagram represent data flow throughout the program. This isn't exact as there are some details I choose to omit to fit it on the slide.]

---
System Overview
Hardware Abstraction Layer
program.c
plcmcu.mcp
plcmcu.h
plcmcu.c
[Speaker Notes: So this is the system that was developed as a whole hardware and software. I tried to keep things simple where possible but the end result is still pretty massive. Arrows in this diagram represent data flow throughout the program. This isn't exact as there are some details I choose to omit to fit it on the slide.]

---
Intermediate Language
- Takes abstract code generated by the GUI editor.
- Runs it as a specific code for underlying hardware.
[Speaker Notes: Ok so when I showed you the tool and hit compile I said it was compiled to “C” but required our framework. Well our framework is what fills in the gaps of our intermediate language. In order to make this tool hardware portable the tool itself as much as possible refers to macros. For example I the tool doesn't actually generate the code for “delay” it just calls a “delay function” that it expects to be implemented by that hardware port. This allows for multiple targets to adjust how many cycles they need to wait to get the same delay time. Likewise I/O pins are configured the same way through header files. In our current MPLab environment our tool generates a Program.c file. This file is referenced by our MPLab project (provided to the end user). plcmcu.h has headers that define ports and timings. The main OS is actually in plcmcu.c. Program.c is actually a subroutine that is called in plcmcu.c, we did it this way so that plcmcu.c can do any number of setup tasks and cleanup tasks when it completes.]

---
Intermediate Language
- program.c
  - The code generated by the editor (when you hit compile)
- plcmcu.h + plcmcu.c
  - The lower level chip support
  - Ports, Timing, Calling your program.c
  - Cleanup operations
[Speaker Notes: Ok so when I showed you the tool and hit compile I said it was compiled to “C” but required our framework. Well our framework is what fills in the gaps of our intermediate language. In order to make this tool hardware portable the tool itself as much as possible refers to macros. For example I the tool doesn't actually generate the code for “delay” it just calls a “delay function” that it expects to be implemented by that hardware port. This allows for multiple targets to adjust how many cycles they need to wait to get the same delay time. Likewise I/O pins are configured the same way through header files. In our current MPLab environment our tool generates a Program.c file. This file is referenced by our MPLab project (provided to the end user). plcmcu.h has headers that define ports and timings. The main OS is actually in plcmcu.c. Program.c is actually a subroutine that is called in plcmcu.c, we did it this way so that plcmcu.c can do any number of setup tasks and cleanup tasks when it completes.]

---
Intermediate Language
What the Intermediate Language Does:
- Hardware Abstraction
  - Chip timing
  - Chip specific ports
- What isn't in the diagram
  - Variable declarations
  - Internal code for each diagram block
  - Graph edges in code (goto)
  - Guard conditions on edges (goto)
[Speaker Notes: AVR's have built in timers, PIC's do not to do timing delays you have to work out the frequency of the crystal and multiply that by 4 to get the clock frequency. Then all instructions in PIC's take 4 clock cycles to finish so you work out your timings from that. You end up looping a bunch of no-ops in assembly. To get timing delays. I didn't want to build this into the tool so this can be left for the specific hardware vendors. Likewise what the port names actually are are left out to be mapped by the hardware manufacturer. Intermediate language also houses many concepts that are abstracted away to make the diagram simpler to read.]

---
Intermediate Language
Going from diagram to code.
void program(void)
{
// BEGIN VARIABLE INITIALIZATIONS //
// END VARIABLE INITIALIZATIONS //
BLUID0:
//////////////////////////////////////
// PROGRAM START //
//////////////////////////////////////
goto BLUID3;
goto EOF;
...
BLUID3:
//////////////////////////////////////
// OUTPUT //
//////////////////////////////////////
PORTOUT = 0;
goto BLUID2;
goto EOF;
EOF:
return;
}

---
Intermediate Language
BLUID5:
//////////////////////////////////
// Block Header //
//////////////////////////////////
(Program Code)
if ( guard condition ) goto BLUID2;
goto EOF;
BLUID2:
//////////////////////////////////
// Block Header //
//////////////////////////////////
(Program Code)
if ( guard condition ) goto BLUID5;
goto EOF;
[Speaker Notes: Structurally in the Intermediate language we start each visual block with a BLUID. This stands for Block Unique Identifier. As such each of these are unique and generated at compile time. You will note that the BLUID's are written as a line label. We do this so that each block can have an edge drawn to it and thus can be entered by a simple goto BLUID#.]

---
Intermediate Language
BLUID5:
//////////////////////////////////
// Block Header //
//////////////////////////////////
(Program Code)
if ( guard condition ) goto BLUID2;
goto EOF;
BLUID2:
//////////////////////////////////
// Block Header //
//////////////////////////////////
(Program Code)
if ( guard condition ) goto BLUID5;
goto EOF;
[Speaker Notes: The next area is the block header. Generally we only use this to visually identify the blocks. Here we put which block the following code generated is for. Example: “Store Block”. It doesn't serve a purpose other than debugging the compiler. Or tracing a code block back to it's diagram coutnerpart.]

---
Intermediate Language
BLUID5:
//////////////////////////////////
// Block Header //
//////////////////////////////////
(Program Code)
if ( guard condition ) goto BLUID2;
goto EOF;
BLUID2:
//////////////////////////////////
// Block Header //
//////////////////////////////////
(Program Code)
if ( guard condition ) goto BLUID5;
goto EOF;
[Speaker Notes: Right after the “Block Header” we have the actual block specific program code. This is different depending on which block we are generating code for and can be arbitrarily long. For example there is no limit on how many assigns can happen in a store block and each store block statement will then appear here in this section. Most blocks in our code however are simple enough and I expect a high number of future blocks to just be macro calls.]

---
Intermediate Language
BLUID5:
//////////////////////////////////
// Block Header //
//////////////////////////////////
(Program Code)
if ( guard condition ) goto BLUID2;
goto EOF;
BLUID2:
//////////////////////////////////
// Block Header //
//////////////////////////////////
(Program Code)
if ( guard condition ) goto BLUID5;
goto EOF;
[Speaker Notes: If an edge is drawn in our diagram where the source is from BLUID5 to BLUID2. We will get a guarded GOTO. The goto fills the transition from one block to another. The guard condition can be any valid C expression. This does present a problem in that if the user does not provide guard conditions that are mutually exclusive the outcome is undefined. This is well noted in the thesis in that our language does not permit this but our compilation tools cannot detect this. I've been informed that checking for mutual exclusion is a very difficult problem and can be turned into a thesis itself.]

---
Intermediate Language
BLUID5:
//////////////////////////////////
// Block Header //
//////////////////////////////////
(Program Code)
if ( guard condition ) goto BLUID2;
goto EOF;
BLUID2:
//////////////////////////////////
// Block Header //
//////////////////////////////////
(Program Code)
if ( guard condition ) goto BLUID5;
goto EOF;
[Speaker Notes: Finally in state machines and flow charts it is understood that if no edges leave a state than we must stay in that state indefinitely. In our Intermediate Language this is accomplished by always inserting a “goto End Of File” at the end after all edge “goto's” have been generated. At the end of the program we insert an appropriate EOF label so all blocks can “stop” if there are no further takeable transitions.]

---
Example
void program(void)
{
// BEGIN VARIABLE INITIALIZATIONS //
// END VARIABLE INITIALIZATIONS //
BLUID0:
//////////////////////////////////////
// PROGRAM START //
//////////////////////////////////////
goto BLUID3;
goto EOF;
...
BLUID3:
//////////////////////////////////////
// OUTPUT //
//////////////////////////////////////
PORTOUT = 0;
goto BLUID2;
goto EOF;
EOF:
return;
}
[Speaker Notes: In the accompanying code section for the blinky light example you can see the output block's code. The start block as you can see contains no code serves only as an entry point and points directly at the output block. As a convenience any edges that are marked with true are generated without the “if” guard condition. Finally in this example the only things in the EOF section of the code is the return statement. EOF's in our current architecture are no different from returns. However it is still nice to have the flexibility to change our minds about this later.]

---
Compilation Steps
- Cycle through and collect all variables
  - Sanity checks
- Find the start block
  - Sanity checks
  - Generate goto edges
- Find remaining blocks
  - Generate associated code
  - Generate guarded goto edges
  - Generate EOF
- Create EOF and return
[Speaker Notes: So what's involved in transforming the diagram into compiled IL code? Because for convenience we don't require the user declare variables in the diagram, it's then up to our compiler to go through every block and collect all the variables and their types used. It then declares each of these at the beginning of the program before the start block. Since it is really cheap we can do one additional sanity check and make sure the user doesn't use one variable name as 2 or more different types in their diagram. The next step is to search through our collection of blocks and find the start blocks. Only one start block can exist which is easy to check so check for that. The start block is always generated before any other block since we need a point of entry. After the start block is generate all the BLUID's and assign the goto edge leaving the start block. Finally for all remaining blocks we generate their associated code, and edges and insert a EOF. Lastly an EOF section of the program is created, in our case we insert a simple return.]

---
Conclusion
- We set out to develop a simpler programming language.
  - Much easier for programmers to express programs.
  - Compared to Ladder Logic we believe Logic Control Chart is much easier to learn and faster to use.
- Developed an entire development enviroment.
  - GUI editor
  - Simulator
  - Compilation Tools
  - Hardware Framework
  - Prototype Reference Platform

---
Future Work
- AVR Target Platform
- The ability to have sub-diagrams
- Make the language provably correct
- Certified PLC programs
- http://github.com/vortex-5/plcthesis

---
Questions?
References
- J. Arlow and I. Neustadt, UML 2 and the Uniﬁed Process: Practical Object-Oriented Analysis and Design (2nd Edition) (Addison-Wesley Object Technology Series). Addison-Wesley Professional, 2005.
- A. B. R. Automation, Rockwell Automation: I/O Adapter Speciﬁcations. Rock-well Automation, 1201 South Second St., Milwaukee, WI 53204-2496, USA.
- W. Bolton, Programmable Logic Controllers, Fourth Edition. Newnes, 2006.
- T. L. Booth, Sequential Machines and Automata Theory. John Wiley and Sons, Inc., 1967.
- M. Corp., “Mitsubishi electric automation: Catalog.” Used image from product catalog only, 01 2009.
- A. J. Crispin, Programmable Logic Control lers and Their Engineering Applications. McGraw-Hill Companies, 1996.
- “How plc’s work.” http://www.plcdev.com/how_plcs_work, 01 2009.
- R. Filer, Programmable Controllers Using Allen-Bradley Slc 500 and Control logix. Englewood Cliffs: Prentice Hall, 2002.