Title
Logic Control Chart
Ladder Control Chart: A Better Visual Language
Presented By: M.A.S.c Candidate FanFan Huang

---
Presentation Outline
- Background Information.
  - What are PLC's?
  - PLC's and their evolution.
- Ladder Logic Visual Language.
  - Quick intro and some examples.
  - What we are hoping to do better.

---
Presentation Outline
- Logic Control Chart
  - The basics of our language.
  - Demo of the tool (Drawing / Compile / Simulate)
  - Logic Control Chart Primitives
- Logic Control Chart Comparison Demos
  - Simple Blinking Light
  - Stepper Motor Controller

---
Presentation Outline
- Hardware Abstraction
  - Hardware Support Framework
  - Intermediate Language
- Summary
  - Entire system and project overview.
- Questions

---
Introduction to PLC's
- Programmable Logic Controllers have existed for over 30 years.
- Used widely in the manufacturing industry.

---
Introduction to PLC's
- PLC's started life as a relay cabinet
- Noisy
- Failed often
- Hard to program
- Hard to isolate hardware failure

---
Modern PLC's

---
Modern PLC's

---
Modern PLC's
- Use ladder logic as the visual programming language.
- Simulates concurrent behaviour
- Executes in scans
Self-Test
Input Scan
Logic Solve
Output Scan

---
Ladder Logic Background
- Ladder logic is an analogy to physical circuits.
- The left most and right most lines are power rails.
- Each circuit is wired on a horizontal “rung”.
- A circuit consists of series loads and exactly one output.
- Loads can be thought of as inputs and can be physical or logical.

---
Elements of Ladder Logic
1
0
in1
1
0
out1

---
Elements of Ladder Logic
in1
in1
out1
1
0

---
Elements of Ladder Logic
in1
1
0
out1
in2

---
Elements of Ladder Logic

---
Logic Control Chart
- A visual metaphor based on State Machines
- Reads like a flow chart
- Based on UML2 specification for State Machine Diagrams
- Goal: Easy!
- UI designed to mimic popular flow charting software like Microsoft Visio, and Open Office Draw.

---
Logic Control Chart
- Tool Demo
- Parts of the UI
- Usage of the Drawing Canvas
- Compiled Code View
- Simulator Trace

---
Logic Control Chart
- Language Concepts and Order of Execution
- Edges
- Start
- Delay
- Input
- Output
- Store

---
Demo Blinky Light

---
Demo Blinky Light
Demo on proto board (slide not shown)

---
Demo Stepper Motor

---
Demo Stepper Motor
Board demo (slide not shown)

---
Ladder Logic Equivalent
S1
Delay
SLatch1
SLatch1
S2
Delay
SLatch2
SLatch2
S3
Delay
SLatch3
SLatch3
S4
Delay
SLatch4
SLatch4
Sets up and latches current state.

---
Ladder Logic Equivalent
SLatch1
BreakS2
NextS2
NextS2
Prepares the next state.
SLatch2
BreakS3
NextS3
NextS3
SLatch3
BreakS4
NextS4
NextS4
SLatch4
BreakS1
NextS1
NextS1

---
Ladder Logic Equivalent
Enforces delay between switching states (prevents stepper motor from running too fast).
Note: S1-S4 only occur for 1 scan it's used to signify the entry into the state.
Slatch1-4 are used to designate running while in the state.
Delay
start
S1
NextS1
Delay
S2
NextS2
Delay
NextS3
Delay
NextS4
S3
S4

---
Ladder Logic Equivalent
Notify we entered the state and breaks any orders to transition back to this state next
SLatch1
BreakS1
SLatch2
BreakS2
SLatch3
BreakS3
SLatch4
BreakS4

---
Ladder Logic Equivalent
Timing delay flip-flop circuit.
Note: Delay is a special output that only goes ON after power is held on for longer than the delay period.
TimerOn
Delay
start
TimerOn
TimerOn
TimerOn
Delay

---
Ladder Logic Equivalent
Send output to the motor. Note: out0-3 are wired to the stepper motor.
SLatch1
out3
SLatch2
out0
SLatch3
out2
SLatch4
out1

---
Intermediate Language
- It's just C with extra functions.
  - C18 compiles C for PIC chips
  - AVR has an equivalent C compiler

---
Intermediate Language
What the Intermediate Language Does:
- Hardware Abstraction
  - Chip timing
  - Chip specific ports
- What isn't in the diagram
  - Variable declarations
  - Internal code for each diagram block
  - Graph edges in code (goto)
  - Guard conditions on edges (goto)

---
Intermediate Language
Gotos?
Source: http://xkcd.com/292/

---
Intermediate Language
BLUID5:
//////////////////////////////////
// Block Header //
//////////////////////////////////
(Program Code)
if ( guard condition ) goto BLUID2;
goto EOF;
BLUID2:
//////////////////////////////////
// Block Header //
//////////////////////////////////
(Program Code)
if ( guard condition ) goto BLUID5;
goto EOF;

---
Intermediate Language
BLUID5:
//////////////////////////////////
// Block Header //
//////////////////////////////////
(Program Code)
if ( guard condition ) goto BLUID2;
goto EOF;
BLUID2:
//////////////////////////////////
// Block Header //
//////////////////////////////////
(Program Code)
if ( guard condition ) goto BLUID5;
goto EOF;

---
Intermediate Langauge
BLUID5:
//////////////////////////////////
// Block Header //
//////////////////////////////////
(Program Code)
if ( guard condition ) goto BLUID2;
goto EOF;
BLUID2:
//////////////////////////////////
// Block Header //
//////////////////////////////////
(Program Code)
if ( guard condition ) goto BLUID5;
goto EOF;

---
Intermediate Langauge
BLUID5:
//////////////////////////////////
// Block Header //
//////////////////////////////////
(Program Code)
if ( guard condition ) goto BLUID2;
goto EOF;
BLUID2:
//////////////////////////////////
// Block Header //
//////////////////////////////////
(Program Code)
if ( guard condition ) goto BLUID5;
goto EOF;

---
Intermediate Language
BLUID5:
//////////////////////////////////
// Block Header //
//////////////////////////////////
(Program Code)
if ( guard condition ) goto BLUID2;
goto EOF;
BLUID2:
//////////////////////////////////
// Block Header //
//////////////////////////////////
(Program Code)
if ( guard condition ) goto BLUID5;
goto EOF;

---
Intermediate Language

---
Intermediate Language
void program(void)
{
// BEGIN VARIABLE INITIALIZATIONS //
// END VARIABLE INITIALIZATIONS //
BLUID0:
//////////////////////////////////////
// PROGRAM START //
//////////////////////////////////////
goto BLUID3;
goto EOF;
...
BLUID3:
//////////////////////////////////////
// OUTPUT //
//////////////////////////////////////
PORTOUT = 0;
goto BLUID2;
goto EOF;
EOF:
return;
}

---
Intermediate Language
- Compilation Sequence:
  - Cycle through and collect all variables
    - Sanity checks
  - Find the start block
    - Sanity checks
    - Generate goto edges
  - Find remaining blocks
    - Generate associated code
    - Generate guarded goto edges
    - Generate EOF
  - Create EOF and return

---
System Overview
Software and Graphical User Interface Layer
Hardware Abstraction Layer
Chip Tools Layer
Tools
Start Block
Store Block
Input Block
Output Block
Delay Block
Canvas
Zoom
Scroll
File Processor
(Save / Load)
Memory
Model
Trace
Engine
program.c
plcmcu.mcp
plcmcu.h
plcmcu.c
Chip Specific C Compiler
Simulator
Compiler

---
Questions?
References
- J. Arlow and I. Neustadt, UML 2 and the Uniﬁed Process: Practical Object-Oriented Analysis and Design (2nd Edition) (Addison-Wesley Object Technology Series). Addison-Wesley Professional, 2005.
- A. B. R. Automation, Rockwell Automation: I/O Adapter Speciﬁcations. Rock-well Automation, 1201 South Second St., Milwaukee, WI 53204-2496, USA.
- W. Bolton, Programmable Logic Controllers, Fourth Edition. Newnes, 2006.
- T. L. Booth, Sequential Machines and Automata Theory. John Wiley and Sons, Inc., 1967.
- M. Corp., “Mitsubishi electric automation: Catalog.” Used image from product catalog only, 01 2009.
- A. J. Crispin, Programmable Logic Control lers and Their Engineering Applications. McGraw-Hill Companies, 1996.
- “How plc’s work.” http://www.plcdev.com/how_plcs_work, 01 2009.
- R. Filer, Programmable Controllers Using Allen-Bradley Slc 500 and Control logix. Englewood Cliffs: Prentice Hall, 2002.